TPV and TPVF SERIES VALVES BIDDING SPECIFICATIONS

Note: These specifications were current at the time of publication but are subject to change at any time without notice. Please confirm the accuracy of these specifications with the manufacturer and/or distributor prior to installation.

The 1" TPV or TPVF Series valve shall be of globe configuration with a variety of body styles including Female x Female, Male x Male, Male x Barb, and Slip by Slip.

Construction: The valve body shall be constructed of corrosion- and UV-resistant PVC material. Design of valve shall be high flow, low friction loss and shall include optional flow control for precise flow adjustment and manual shut off. Valve shall have patented debris tolerant DBS Technology™ to accommodate dirty water conditions. The valve shall have a self-cleaning, stainless-steel metering pin to protect bleed ports and to purge contaminants without the use of a filter screen. Valve shall have internal and external bleed for manual operation and flushing. Slip models will include patent pending Glue Stop™ to ensure downstream exhaust ports do not get clogged upon installation. Valve shall have a removable tamper-resistant flow control handle. Valve shall have a rugged, double-beaded SANTOPRENE® diaphragm. Valve shall have a positive self aligning bonnet with captured screws. Valve shall have a high-strength, ribbed bonnet. Valve shall be serviceable without needing to be removed from system. Valve shall be powered by a 24 V ac encapsulated solenoid, 0.4 amp inrush and 0.2 amp holding current.

Operation: Valve shall have a working pressure range from 10 psi minimum to 175 psi maximum and recommended flow range from 0.1 to 40 GPM.